A Powerful, Robust Connection:

Logitech Advanced 2.4 GHz Wireless Technology

Wireless networks. Cell phones. Copy machines. Fax machines. Today’s busy offices have made the operation of cordless computer peripherals—such as keyboards and mice—increasingly subject to interference. Some technologies have been developed to operate in this crowded wireless landscape. But only Logitech advanced 2.4 GHz technology provides high-performance and longer battery life at an affordable price.

As a world leader in the development of cordless technologies, Logitech is constantly developing new ways to bring the benefits of cordless products to businesses. Now, Logitech introduces the company’s latest advancement in 2.4 GHz technology.

Logitech advanced 2.4 GHz wireless technology provides a powerful, robust connection with virtually no delays or dropouts (compared to conventional 2.4 GHz and 27 MHz wireless technologies) – even in the busiest wireless environments.

## Inside the technology

Logitech advanced 2.4 GHz technology is the essential ingredient in the company’s cordless mice and keyboard products. Logitech 2.4 GHz wireless technology uses frequencies that are available for electronics in all countries of the world. Similar to Bluetooth®, Logitech’s technology uses frequency-hopping and error-correction techniques, but it also uses a proprietary protocol and architecture for RF communication that conserves battery life and reduces latency.

In particular, Logitech advanced 2.4 GHz wireless technology hops at 250 times/sec and supports bi-directional data transmission with error correction to maintain a reliable RF link. And Logitech’s architecture automatically pairs your peripheral to the provided transceiver that is attached to your computer, while avoiding conflicts with other devices. In other words, when you use a Logitech peripheral with advanced 2.4 GHz technology, you can be certain that when you move your mouse or type on your keyboard, your commands will be carried out instantaneously.

Logitech’s proprietary wireless protocol is used together with a high-performance RF transceiver. This is a highly integrated, single-chip transceiver that operates in the 2.4 GHz ISM band and is ideally suited for the most demanding applications. In addition to the technical features described above, this technology also provides the lowest-power RF solution on the market today, translating into significantly longer battery life.

| Feature | Logitech advanced 2.4 GHz wireless technology | Bluetooth |
| --- | --- | --- |
| Range | 10 m | 10 – 100 m |
| Bandwidth | 2 Mbps bursts | 1 – 3 Mbps bursts |
| Latency at reconnection | < 90 ms | .5 – 2 seconds |
| Interference resistance | Best | Best |
| Battery life | Best | Good |
| Report rate | 125 rpt/s or faster | 80 rpt/s |
| USB interface | FS | FS |